Class description

Elements:

molar_weight(self, element):
        '''
        Input (self, element)
        A dictionary containing molar weights of most elements, and additional
        made up elements to make it possible to use in fuel analysis. These
        are ash, VM and FC, and each has been given the molecular weight of
        0.0. H2O is also present.

        By Angus Malmgren on 2015/02/06
        Updated by Alf Malmgren 2020-11-20, added CO, CO2, H2, CH4 and SO2
        '''

molesperkg(self, analysis):
        '''
        molesperkg - calculates the number of moles there is of each
        element in a kg of fuel
        input:
        analysis - This is a library contining the analysis of the fuel
        of the form: analysis = {'C':inData['C']}
        output:
        moles - This is a library contining the number of moles of each
        element per kg:
        moles = {'C':inData['C']*10/molar_weight['C']}

        By Angus Malmgren on 2015/02/06
        '''

NASA_coeff:

CP_coeff_NASA(self,gas):
        '''
        Input: (self,gas)
        This routine defines the polynomial coefficients for Cp of a number
        of gases at atmospheric pressure and at the temperature T in
        degrees C.
        The return value is Cp/R and is dimensionless. Multiply with
        R=8.31451, gives Cp in J/kg/K.

        The Cp/R at the temperature T is calculated as:

        Cp/R = A+T(B+T(C+T(D+T*E)))

        The average Cp between T1 and T2 can be calculated as:

        B C (T23-T13) D (T24-T14) E (T25-T15)
     Cp(ave)/R = A + --- (T2-T1) + --- ----------- + ---- ------------- + --- --------------
        2 3 (T2-T1) 4 (T2-T1) 5 (T2-T1)

        Input:
        gas - A string defining which gas that is requested.
        Allowed strings are: 'CO2', 'H2O', 'O2', 'N2' or 'SO2'

        Output:
        AL,BL,CL, DL, EL = The polynomial coefficients for the chosen
        gas for >1000K
        AH,BH,CH,DH,EH = The polynomial coefficients for the chosen
        gas for <1000K
        MW = The moleqular weight for the gas
        flag = flag=0 success
        flag=1 could not find coefficients for
        this gas

        Example: AL,BL,CL,DL,EL,AH,BH,CH,DH,EH,MW,flag = CP_coeff_NASA('CO2')

        By Alf Malmgren on 2015/02/17.
        Update and N2 corrected 2020-11-20 by alf Malmgren
        '''

polyAveNASA (self,T0,T1,AL,BL,CL,DL,EL,AH,BH,CH,DH,EH):
        '''
        Input: (self,T0,T1,AL,BL,CL,DL,EL,AH,BH,CH,DH,EH)
        This function calculates the average value of the dependent variable, V,
        between two gas temperatures, calculated using the integrated form of the
        polynomial based on coefficients from NASA. There are two sets of
        coefficients for temperatures over and under 1000 K.

        Input: T0, T1 =independent variable (for example the lowest and highest
        temperatures in the interval studied (in degrees C))

        AL,BL,CL,DL,EL and AH,BH,CH,DH,EH are the polynomial coefficients for
        low temperatures (<1000 K) and high (>1000K) of the form

        3 3 4 4 5 5
        B C (T1 - T0 ) D (T1 - T0 ) E (T1 - T0 )
        A + - * (T1 + T0) + - * ---------- + - * ---------- + - * ----------
        2 3 (T1 - T0) 4 (T1 - T0) 5 (T1 - T0)

        Last edited by Alf Malmgren on 2015/01/16
        '''

 gas_cp (self, T0, T1):
        '''
        Input: (self, T0, T1)

        Calculates the lower and higher temperature CP coefficients from NASA
        calling CP_coeff_NASA

        By Angus Malmgren
        On 2015/02/18
        '''